## Slide 1: Discuss in detail about Software Requirement Analysis ?

## Slide 2: Requirements engineering
The process of establishing the services that the customer requires from a system and the constraints under which it operates and is developed.
The requirements themselves are the descriptions of the system services and constraints that are generated during the requirements engineering process.

## Slide 3: What is a requirement?
It may range from a high-level abstract statement of a service or of a system constraint to a detailed mathematical functional specification.
This is inevitable as requirements may serve a dual function
  May be the basis for a bid for a contract - therefore must be open to interpretation;
  May be the basis for the contract itself - therefore must be defined in detail;
  Both these statements may be called requirements.

## Slide 4: Requirements abstraction (Davis)

## Slide 5: Types of requirement
User requirements
  Statements in natural language plus diagrams of the services the system provides and its operational constraints. Written for customers.
System requirements
  A structured document setting out detailed descriptions of the system’s functions, services and operational constraints. Defines what should be implemented so may be part of a contract between client and contractor.

## Slide 6: Requirements readers

## Slide 7: Functional and non-functional requirements
Functional requirements
  Statements of services the system should provide, how the system should react to particular inputs and how the system should behave in particular situations.
Non-functional requirements
  constraints on the services or functions offered by the system such as timing constraints, constraints on the development process, standards, etc.
Domain requirements
  Requirements that come from the application domain of the system and that reflect characteristics of that domain.

## Slide 8: Functional requirements
Describe functionality or system services.
Depend on the type of software, expected users and the type of system where the software is used.
Functional user requirements may be high-level statements of what the system should do but functional system requirements should describe the system services in detail.

## Slide 9: The LIBSYS system
A library system that provides a single interface to a number of databases of articles in different libraries.
Users can search for, download and print these articles for personal study.

## Slide 10: Examples of functional requirements
The user shall be able to search either all of the initial set of databases or select a subset from it.
The system shall provide appropriate viewers for the user to read documents in the document store.
Every order shall be allocated a unique identifier (ORDER_ID) which the user shall be able to copy to the account’s permanent storage area.

## Slide 11: Non-functional requirements
These define system properties and constraints e.g. reliability, response time and storage requirements. Constraints are I/O device capability, system representations, etc.
Process requirements may also be specified mandating a particular CASE system, programming language or development method.
Non-functional requirements may be more critical than functional requirements. If these are not met, the system is useless.

## Slide 12: Requirements measures

## Slide 13: Requirements interaction
Conflicts between different non-functional requirements are common in complex systems.
Spacecraft system
  To minimise weight, the number of separate chips in the system should be minimised.
  To minimise power consumption, lower power chips should be used.
  However, using low power chips may mean that more chips have to be used. Which is the most critical requirement?

## Slide 14: Domain requirements
Derived from the application domain and describe system characteristics and features that reflect the domain.
Domain requirements be new functional requirements, constraints on existing requirements or define specific computations.
If domain requirements are not satisfied, the system may be unworkable.

## Slide 15: Library system domain requirements
There shall be a standard user interface to all databases which shall be based on the Z39.50 standard.
Because of copyright restrictions, some documents must be deleted immediately on arrival. Depending on the user’s requirements, these documents will either be printed locally on the system server for manually forwarding to the user or routed to a network printer.

## Slide 16: Domain requirements problems
Understandability
  Requirements are expressed in the language of the application domain;
  This is often not understood by software engineers developing the system.
Implicitness
  Domain specialists understand the area so well that they do not think of making the domain requirements explicit.

## Slide 17: User requirements
Should describe functional and non-functional requirements in such a way that they are understandable by system users who don’t have detailed technical knowledge.
User requirements are defined using natural language, tables and diagrams as these can be understood by all users.

## Slide 18: Problems with natural language
Lack of clarity
  Precision is difficult without making the document difficult to read.
Requirements confusion
  Functional and non-functional requirements tend to be mixed-up.
Requirements amalgamation
  Several different requirements may be expressed together.

## Slide 19: Requirement problems
Database requirements includes both conceptual and detailed information
  Describes the concept of a financial accounting system that is to be included in LIBSYS;
  However, it also includes the detail that managers can configure this system - this is unnecessary at this level.
Grid requirement mixes three different kinds of requirement
  Conceptual functional requirement (the need for a grid);
  Non-functional requirement (grid units);
  Non-functional UI requirement (grid switching).

## Slide 20: Guidelines for writing requirements
Invent a standard format and use it for all requirements.
Use language in a consistent way. Use shall for mandatory requirements, should for desirable requirements.
Use text highlighting to identify key parts of the requirement.
Avoid the use of computer jargon.

## Slide 21: System requirements
More detailed specifications of system functions, services and constraints than user requirements.
They are intended to be a basis for designing the system.
They may be incorporated into the system contract.
System requirements may be defined or illustrated using system models discussed in Chapter 8.

## Slide 22: Requirements and design
In principle, requirements should state what the system should do and the design should describe how it does this.
In practice, requirements and design are inseparable
  A system architecture may be designed to structure the requirements;
  The system may inter-operate with other systems that generate design requirements;
  The use of a specific design may be a domain requirement.

## Slide 23: Structured language specifications
The freedom of the requirements writer is limited by a predefined template for requirements.
All requirements are written in a standard way.
The terminology used in the description may be limited.
The advantage is that the most of the expressiveness of natural language is maintained but a degree of uniformity is imposed on the specification.

## Slide 24: Form-based specifications
Definition of the function or entity.
Description of inputs and where they come from.
Description of outputs and where they go to.
Indication of other entities required.
Pre and post conditions (if appropriate).
The side effects (if any) of the function.

## Slide 25: Graphical models
Graphical models are most useful when you need to show how state changes or where you need to describe a sequence of actions.
Different graphical models are explained in Chapter 8.

## Slide 26: Sequence diagram of ATM withdrawal

## Slide 27: PDL interface description

## Slide 28: The requirements document
The requirements document is the official statement of what is required of the system developers.
Should include both a definition of user requirements and a specification of the system requirements.
It is NOT a design document. As far as possible, it should set of WHAT the system should do rather than HOW it should do it

## Slide 29: Users of a requirements document

## Slide 30: IEEE requirements standard
Defines a generic structure for a requirements document that must be instantiated for each specific system.
  Introduction.
  General description.
  Specific requirements.
  Appendices.
  Index.

## Slide 31: Requirements document structure
Preface
Introduction
Glossary
User requirements definition
System architecture
System requirements specification
System models
System evolution
Appendices
Index

## Slide 32: Requirements analysis process
the problem
requirements
elicitation
build a
prototype
create
analysis
models
develop
specification
validation
management

## Slide 33: Requirements engineering - I
Inception —ask a set of questions that establish …
  basic understanding of the problem
  the people who want a solution
  the nature of the solution that is desired, and
  the effectiveness of preliminary communication and collaboration between the customer and the developer
Elicitation —elicit requirements from all stakeholders
Elaboration —create an analysis model that identifies data, function and behavioral requirements
Negotiation —agree on a deliverable system that is realistic for developers and customers

## Slide 34: Requirements engineering - II
Specification —can be any one (or more) of the following:
  A written document
  A set of models
  A formal mathematical
  A collection of user scenarios (use-cases)
  A prototype
Validation —a review mechanism that looks for
  errors in content or interpretation
  areas where clarification may be required
  missing information
  inconsistencies (a major problem when large products or systems are engineered)
  conflicting or unrealistic (unachievable) requirements.
Requirements management